## Slide 1: NETWORK TOPOLOGY DESIGN AT 27,000 KM/HOUR Debopam Bhattacherjee, Ankit Singla. Department of Computer Science, ETH Zürich
PRESENTER: OGHENEVOVWE A. IKUMARIEGBE

## Slide 2: LEO NETWORKS
This paper was aimed at exploring network topology design for LEO constellation networks.
Key observation: Increasing the capacity of the inter-satellite network would increase throughput between end-to-end ground stations.

## Slide 3: MAINSTREAM IDEA: GRID-LIKE STRUCTURE
A topology design consisting of links to neighboring satellites in the four directions (a grid-like) structure, +Grid.
However, such design is limiting and underutilizes the network since an ISL has a farther reach than the neighboring satellite.

## Slide 4: AN EXAMPLE OF A LEO SATELLITE NETWORK
Kuiper
 | Phase A | Phase B | Phase C
Orbital Planes | 34 | 36 | 28
Satellite per plane | 34 | 35 | 28
Altitude (km) | 630 | 610 | 590
Inclination | 51.9 | 42 | 33

## Slide 5: KEY POINTS ABOUT A LEO SATELLITE NETWORK
Satellites move very fast.
ISLs are needed because using just GS up-and-down links would incur high overhead and latency.
ISLs are constrained mainly by visibility and power.
Less hops implies that less satellites are used to carry a particular traffic.

## Slide 6: VISIBILITY
For a satellite with an altitude of 550 km, the maximum ISL length is

## Slide 7: Investigating traditional network design approaches
The network design approaches for terrestrial networks were evaluated for a dynamic, satellite network.
Integer linear programming
Random regular graphs
Ant-colony optimization

## Slide 8: OPTIMIZATION PROBLEM
Inputs
Satellites trajectories.
Number of inter-satellite connection units
Target traffic matrix between terrestrial end points
Goal: A network design that minimizes latency and hop-count in end-end paths.

## Slide 9: Integer LINEAR PROGRAMMING
Inputs
L : Maximum number of ISLs allowed per satellite.
vab : Is sata visible to satb and within its range?
dab : Linear distance between satellite sata and satb.
A traffic matrix, H , between terrestrial sites.
Outputs
yab
xstab
Intermediate
where
S – stretch, ratio of network path to geodesic path
B – hop count
– weight for the stretch
Objective Function

## Slide 10: Satellite path vs geodesic distance
Customized ILP: Satellites “too far away” from the geodic between endpoints shouldn’t carry traffic.

## Slide 11: Results and issues
Results
For 20 cities, ILP’s +Grid’s
Issues
Poor scalability.
Temporal dynamics : too many link changes in a minute

## Slide 12: Random Regular Graphs (Customized)
Idea: Sampling permissible edges.
Constraint: Only satellites with fewer than 4 connections are added.

## Slide 13: Results and issues
Results
Decrease hop count (median) by 53% by
sacrificing median stretch by 11%
RRG’s +Grid’s .
RRG’s +Grid’s
Issues
Temporal dynamics
Inflexibility.

## Slide 14: ANT-COLONY OPTIMIZATION
Optimized from random graphs.
Conclusion.
Works well for small problem sizes, but doesn’t converge for big ones. It also causes huge link churn.

## Slide 15: NOVEL APPROACH : MOTIFS
Motifs : repeated connectivity pattern (3-satellite, 2-links) across the constellation,. Can be considered as a generalization of +Grid

## Slide 16: OBSERVATIONS AND APPROACH
APPROACH ONE:
Evaluating all possible motifs to select one with the best performance
Observation : There are fewer in-range satellites at the Equator. So, selecting motifs near the Equator ensures that links are kept throughout the constellation, that is, no link churn.
Summary
A satellite at the Equator , e
Se - the set of all satellites within e’s range
Set of all motifs,
Output best motif,

## Slide 17: PERFORMANCE AT AN Arbitrary snapshot

## Slide 18: PERFORMANCE OVER TIME
The best motif achieves 44% (43%) lower than +Grid in the median (95th percentile).

## Slide 19: PERFORMANCE OVER DIFFERENT CONSTELLATION SIZES

## Slide 20: PERFORMANCE OVER DIFFERENT INCLINATIONS
The median improvement in M1 going from +Grid to motifs is 46% for the polar constellation, compared to 44.5% for the 53° one

## Slide 21: POWER LIMITATIONS – MAXIMUM ISL RANGE AT 3000 km

## Slide 22: GDP TRAFFIC MATRIX
Scale city-city traffic volume by the products of city pairs.
Result: For the 402 inclined constellation, the best motif achieves 34% lower (better) than +Grid for this trac matrix.

## Slide 23: APPROACH 2
Based on previous observation, different motifs can be computed for different latitudes.
Issues: Huge, impractical computation needed,

## Slide 24: APPROACH 3
Different motifs computed for different latitudes zones.
For 53° constellation, a zone width of 18° results in 3 zones: 0-18°, 18-36°, 36-53°

## Slide 25: IMPROVEMENTS SATURATE AFTER THREE ZONES

## Slide 26: STARLINK AND KUIPER - optimizations

## Slide 27: STRETCH AND HOP counts
, , improvements are respectively 48%, 30%, and 20% over +Grid

## Slide 28: QUESTIONS
Why do they mention that longer ISLs ranges are needed when there’s a visibility constraint?
Answer: It was mentioned for the Telesat satellite constellation. It has a higher altitude and hence a longer ISL range.

## Slide 29: THANK YOU!